Chefmaster Fly Killers

Instruction Manual

Model

HEA780 – Aluminum 50m2 Coverage

HEA325 - Aluminum 50m2 Coverage

HEA781 – Stainless Steel 50m2 Coverage

HEA782 – Aluminum 100m2 Coverage

HEA783 – Stainless Steel 100m2 Coverage

HEA784 – Aluminum 150m2 Coverage

HEA785 – Stainless Steel 150m2 Coverage

Thank you for purchasing your Chefmaster Fly Killer. To make full use of the product please read this manual carefully before using the product and keep it safe for future reference.

Safety Tips

- If you find any damage when the product is unpacked, contact your Chefmaster supplier within 24 hours of receipt of goods

- Repairs should always be carried out by a qualified technician

- Do not use this product outside

- Install out of reach of Children

- Install at least 1m away from food preparation areas

- Do not use near flammable objects

- Always switch off and unplug the unit before cleaning

- If the power cord becomes damaged it must be replaced by a qualified technician

- This product is not designed to be used by persons with reduced physical or mental capabilities, lack of experience or knowledge, unless they are given suitable supervision, this includes children.

- This product is designed for indoor use only.

Pack Contents

- 1 x Chefmaster Fly Killer

- 1 x Hanging chain

Before Use

- Remove all packaging including all protective plastic, from your Chefmaster Fly Killer

- For best results install your fly killer in the darkest part of the room, 1m way from any food preparation areas

Operation

- Ensure the fly killer is plugged in and the power is on

- The light will then come on and the grid will be electrically charged

Cleaning & Maintenance

- Before cleaning disconnect the fly killer from the electricity supply.

- Clean the collection tray with soapy warm water regularly

- DO NOT submerge the fly killer in water or use water sprays to clean it

Changing the Bulb

- Unscrew the 2 screws on the top of the outer metal grid

- The grid will then open downwards

- Remove bulb and replace

- Replace the out metal grid into its original position

Troubleshooting

| Fault | Possible Cause | Solution |
| --- | --- | --- |
| Unit is not working | The unit is not switched on The plug or lead are damaged The fuse has blown Bulb is not working | Check the unit is plugged in and switched on Contact your Chefmaster distributor Replace the fuse Replace the bulb |

Transportation and Storage

Please handle your fly killer with care to prevent any damage to the unit and internal parts. The fly killer should be stored somewhere which is ventilation and non-corrosive gas.

Do not store any flammable objects near the equipment.

Technical Information

HEA780 – Aluminum 50m2 Coverage

Voltage ~230v 50/60Hz

Power 11watt

Weight 1.95kg

Dimensions 340 x 100 x 265mm

HEA325 - Aluminum 50m2 Coverage

Voltage ~230v 50/60Hz

Power 11watt

Weight 1.95kg

Dimensions 340 x 100 x 265mm

HEA781 – Stainless Steel 50m2 Coverage

Voltage ~230v 50/60Hz

Power 11watt

Weight 2.5kg

Dimensions 390 x 115 x 265mm

HEA782 – Aluminum 100m2 Coverage

Voltage ~230v 50/60Hz

Power 22watt

Weight 2.2kg

Dimensions 335 x 100 x 265mm

HEA783 – Stainless Steel 100m2 Coverage

Voltage ~230v 50/60Hz

Power 22watt

Weight 2.6kg

Dimensions 395 x 115 x 265mm

HEA784 – Aluminum 150m2 Coverage

Voltage ~230v 50/60Hz

Power 33watt

Weight 2.7kg

Dimensions 490 x 100 x 265mm

HEA785 – Stainless Steel 150m2 Coverage

Voltage ~230v 50/60Hz

Power 33watt

Weight 3.3kg

Dimensions 550 x 115 x 265mm

- Chefmaster fly killer is supplied with a 3 pin plug and lead with a 13 amp fuse

- Appliance must be earthed

- If in doubt contact a qualified electrician or your Chefmaster distributor

Disposal

Under WEEE regulations this product must not be disposed of as household waste. To prevent damage to the environment and humans this product must be disposed of in an approved and environmentally friendly recycling process. For more information on how to dispose of this correctly please contact your Chefmaster distributor or local authority responsible for waste disposal.

Compliance

All Chefmaster parts and products have under gone a stringent testing process to ensure that comply with all European standards and specifications.

All Chefmaster products carry the CE approval symbol.